## Slide 1
Chapter 4
Bit Manipulations

## Slide 2
Introduction to Multiplication
Decision-making capabilities are essential in processors.
Multiplication is a fundamental process we learned early on.
Commonly performed through algorithms to convey to processors.
unioffaisalabad
www.tuf.edu.pk
Multiplication Algorithm in Processors
Familiar Multiplication Technique
Multiply by each digit of the multiplier.
Write intermediate results aligned by place value.
Sum the intermediate results for the final answer.

## Slide 3
unioffaisalabad
www.tuf.edu.pk
Binary Multiplication Example
Multiplicand: 110111011101 (13 in decimal)
Multiplier: 010101010101 (5 in decimal)
Expected Result: 010000010100000101000001 (65 in decimal)
1101
x 0101
-------
1101
0000x
1101xx
0000xxx
-------
01000001

## Slide 4
unioffaisalabad
www.tuf.edu.pk
Steps in Binary Multiplication Algorithm
Take the first digit of the multiplier and multiply by the multiplicand.
Place the multiplicand below the line if the digit is 1.
Shift left for each subsequent digit, adding crosses for 0s.
Sum all intermediate results.
Observations in Binary Multiplication
Multiplying by 1 gives the multiplicand; by 0 gives 0.
Results shift left for each digit in the multiplier.
No actual multiplication; only addition and shifting needed.
Crosses are treated as zeros in the final addition.

## Slide 5
unioffaisalabad
www.tuf.edu.pk
Need for Shifting Instructions
Essential for shifting the multiplicand.
Enables bit manipulation for efficient calculations.
Necessary for checking each bit of the multiplier.

## Slide 6
The set of shifting and rotation instructions is one of the most useful set in any processor’s instruction set.
They simplify really complex tasks to a very neat and concise algorithm.
The following shifting and rotation operations are available in our processor.
unioffaisalabad
www.tuf.edu.pk
Shifting and Rotations

## Slide 7
The shift logical right operation inserts a zero from the left and moves every bit one position to the right and copies the rightmost bit in the carry flag.
Imagine that there is a pipe filled to capacity with eight balls. The pipe is open from both ends and there is a basket at the right end to hold anything dropping from there.
The operation of shift logical right is to force a white ball from the left end.
The operation is depicted in the following illustration.
White balls represent zero bits while black balls represent one bits.
Sixteen bit shifting is done the same way with a pipe of double capacity.
unioffaisalabad
www.tuf.edu.pk
1. Shift Logical Right (SHR)

## Slide 8
The shift logical left operation is the exact opposite of shift logical right.
In this operation the zero bit is inserted from the right and every bit moves one position to its left with the most significant bit dropping into the carry flag.
Shift arithmetic left is just another name for shift logical left.
The operation is again exemplified with the following illustration of ball and pipes.
unioffaisalabad
www.tuf.edu.pk
2. Shift Logical Left (SHL) / Shift Arithmetic Left (SAL)

## Slide 9
A signed number holds the sign in its most significant bit.
If this bit was one a logical right shifting will change the sign of this number because of insertion of a zero from the left.
The sign of a signed number should not change because of shifting.
The operation of shift arithmetic right is therefore to shift every bit one place to the right with a copy of the most significant bit left at the most significant place.
The bit dropped from the right is caught in the carry basket.
The sign bit is retained in this operation.
The operation is further illustrated below.
unioffaisalabad
www.tuf.edu.pk
3. Shift Arithmetic Right (SAR)

## Slide 10
The left shifting operation is basically multiplication by 2 while the right shifting operation is division by two.
However for signed numbers division by two can be accomplished by using shift arithmetic right and not shift logical right.
The left shift operation is equivalent to multiplication except when an important bit is dropped from the left.
The overflow flag will signal this condition if it occurs and can be checked with JO.
For division by 2 of a signed number logical right shifting will give a wrong answer for a negative number as the zero inserted from the left will change its sign.
To retain the sign flag and still effectively divide by two the shift arithmetic right instruction must be used on signed numbers.
unioffaisalabad
www.tuf.edu.pk

## Slide 11
In the rotate right operation every bit moves one position to the right and the bit dropped from the right is inserted at the left.
This bit is also copied into the carry flag.
The operation can be understood by imagining that the pipe used for shifting has been molded such that both ends coincide.
Now when the first ball is forced to move forward, every ball moves one step forward with the last ball entering the pipe from its other end occupying the first ball’s old position.
The carry basket takes a snapshot of this ball leaving one end of the pipe and entering from the other.
unioffaisalabad
www.tuf.edu.pk
1. Rotate Right (ROR)

## Slide 12
In the operation of rotate left instruction, the most significant bit is copied to the carry flag and is inserted from the right, causing every bit to move one position to the left.
It is the reverse of the rotate right instruction.
Rotation can be of eight or sixteen bits.
The following illustration will make the concept clear using the same pipe and balls example.
unioffaisalabad
www.tuf.edu.pk
2. Rotate Left (ROL)

## Slide 13
In the rotate through carry right instruction, the carry flag is inserted from the left, every bit moves one position to the right, and the right most bit is dropped in the carry flag.
Effectively this is a nine bit or a seventeen bit rotation instead of the eight or sixteen bit rotation as in the case of simple rotations.
Imagine the circular molded pipe as used in the simple rotations but this time the carry position is part of the circle between the two ends of the pipe.
Pushing the carry ball from the left causes every ball to move one step to its right and the right most bit occupying the carry place.
The idea is further illustrated below.
unioffaisalabad
www.tuf.edu.pk
3. Rotate Through Carry Right (RCR)

## Slide 14
The exact opposite of rotate through carry right instruction is the rotate through carry left instruction.
In its operation the carry flag is inserted from the right causing every bit to move one location to its left and the most significant bit occupying the carry flag.
The concept is illustrated below in the same manner as in the last example.
unioffaisalabad
www.tuf.edu.pk
4. Rotate Through Carry Left (RCL)

## Slide 15
unioffaisalabad
www.tuf.edu.pk
Multiplication Algorithm in Assembly Language
The algorithm simplifies traditional multiplication.
Accumulates results to avoid storing intermediate answers.
Example used: Multiplication of binary numbers 1101 (13) and 0101 (5).
1101 = 13 Accumulated Result
0101 = 5
----- 0 (Initial Value)
1101 = 13 0 + 13 = 13
0000x = 0 13 + 0 = 13
1101xx = 52 13 + 52 = 65
0000xxx = 0 65 + 0 = 65 (Answer)

## Slide 16
Accumulated Result
Initialize result to zero.
Check the rightmost bit of the multiplier:
  If 1, add multiplicand to result.
  If 0, perform no addition.
Always left shift the multiplicand.
unioffaisalabad
www.tuf.edu.pk
Modified Multiplication Process

## Slide 17
Steps of the Algorithm
Shift the multiplier to the right.
If Carry Flag (CF) = 1, add the multiplicand to the result.
Shift the multiplicand to the left.
Repeat for as many bits as there are in the multiplier.
Note: For 8-bit multiplication, repeat 8 times; for 16-bit, repeat 16 times.
unioffaisalabad
www.tuf.edu.pk
Algorithm Steps

## Slide 18
Importance of Shifting
Right shifting forces the rightmost bit to drop into the carry flag.
Use JC instruction to check the carry flag (rightmost bit).
Left shifting the multiplicand prepares it for the next bit position.
unioffaisalabad
www.tuf.edu.pk
Role of Shifting Operations

## Slide 19
[org 0x100]
jmp start
multiplicand: db 13 ; 4bit multiplicand
multiplier: db 5 ; 4bit multiplier
result: db 0 ; 8bit result
start: mov cl, 4 ; initialize bit count
mov bl, [multiplicand] ; load multiplicand in bl
mov dl, [multiplier] ; load multiplier in dl
checkbit: shr dl, 1 ; move rightmost bit to carry
jnc skip ; skip addition if bit is zero
add [result], bl ; accumulate result
skip: shl bl, 1 ; shift multiplicand left
dec cl ; decrement bit count
jnz checkbit ; repeat if bits left
mov ax, 0x4c00 ; terminate program
int 0x21
unioffaisalabad
www.tuf.edu.pk
Assembly Code for 4-bit Multiplication

## Slide 20
Understanding SHR and SHL
SHR (Shift Logical Right): Divides operand by 2; remainder in carry flag.
SHL (Shift Logical Left): Multiplies operand by 2; shifts result to the left.
unioffaisalabad
www.tuf.edu.pk
SHR and SHL Instructions

## Slide 21
unioffaisalabad
www.tuf.edu.pk
Extended Operations in Multiplication
Introduction to Extended Operations
Initial focus on 4-bit multiplication for simplicity.
Real advantage lies in multiplying larger numbers.
Assembly language offers basic building blocks for complex operations.
Expanding Multiplication to Larger Bit Sizes
Multiplying Larger Numbers
Can extend multiplication to 16-bit or larger numbers.
Aim: Multiply 16-bit numbers to produce a 32-bit result.
Need for 32-bit shifting and addition operations.

## Slide 22
Why 32-bit Operations?
Shifting 16-bit numbers in a 16-bit space risks losing significant bits.
Place 16-bit numbers in 32-bit space to prevent loss of valuable bits.
Valuable bits: any bit that is '1'; dropping them leads to incorrect results.
unioffaisalabad
www.tuf.edu.pk
Importance of 32-bit Operations

## Slide 23
Example: Multiplying by Two
Consider the number 40000 (0x9C40 in hexadecimal).
Binary representation: 1001110001000000.
Shifting left to multiply by 2 results in: 0011100010000000.
Note: Leftmost '1' drops into the carry flag.
unioffaisalabad
www.tuf.edu.pk
Example of Shifting in Extended Operations

## Slide 24
Incorrect Results from Shifting
Expected result: 0x13880 (80000 in decimal).
Actual result after shifting: 0x3880 (14464 in decimal).
Highlights the importance of using the correct bit-width for operations.
unioffaisalabad
www.tuf.edu.pk
Consequences of Incorrect Shifting

## Slide 25
unioffaisalabad
www.tuf.edu.pk
Extended Shifting in Assembly Language
What is Extended Shifting?
Utilize basic shifting and rotation instructions.
Shift 32-bit numbers in memory word by word.
Limited by architecture to perform word operations.

## Slide 26
Algorithm Overview
Code Example:
    num1: dd 40000
    shl word [num1], 1
    rcl word [num1+2], 1
unioffaisalabad
www.tuf.edu.pk
Shifting a 32-bit Number
DD directive reserves 32-bit space.
Lower word at num1, upper word at num1 + 2.
Shift left the lower word and rotate carry into the upper word.

## Slide 27
Illustration: Diagram showing two pipes:
Left pipe: Upper half of the number.
Right pipe: Lower half of the number.
First instruction (shl): Shift lower word left, drop MSB into carry.
Second instruction (rcl): Push carry into the LSB of the upper word.
unioffaisalabad
www.tuf.edu.pk
How Shifting Works

## Slide 28
Code Example:
      num1: dd 40000
      shr word [num1+2], 1
      rcr word [num1], 1
unioffaisalabad
www.tuf.edu.pk
Shifting Right Process
shr: Shift upper word right, placing LSB in carry.
rcr: Push carry into the lower word's MSB.
Important: Always shift upper half first to maintain integrity.

## Slide 29
Handling Signed Numbers
Use sar (shift arithmetic right) for signed numbers.
Ensures the sign bit is preserved during right shifts.
Scalability of Extended Shifting
Beyond 32 Bits
The method can be extended to shift any size, e.g., 1024 bits.
Repeat the second instruction as needed for larger shifts.
Achieve unlimited bit manipulation with minimal instructions.
unioffaisalabad
www.tuf.edu.pk
Signed Shifting Consideration

## Slide 30
Why Extend Addition and Subtraction?
Essential for multiplying 16-bit numbers producing 32-bit results.
Allows for the addition of larger numbers than the standard operand size.
Introduces new instructions to handle carry and borrow.
unioffaisalabad
www.tuf.edu.pk
Extended Addition and Subtraction
The ADC Instruction
Add with Carry (ADC)
Combines three operands: two explicit and one implicit (carry flag).
Used to ensure that carry from previous addition is accounted for.
Example: ADC AX, BX adds carry flag to AX before adding BX.

## Slide 31
Algorithm for 32-bit Addition
Add lower halves using normal addition.
Use ADC for upper halves to account for any carry from lower halves.
Code Example:
      dest: dd 40000
      src: dd 80000
      mov ax, [src]
      add word [dest], ax
      mov ax, [src+2]
      adc word [dest+2], ax
unioffaisalabad
www.tuf.edu.pk
Extended Addition Algorithm

## Slide 32
Managing Overflow in Addition
Last carry may remain in the carry flag.
Can be tested for overflow conditions after operations.
Essential for managing larger calculations.
The SBB Instruction
Subtract with Borrow (SBB)
Functions similarly to ADC, but for subtraction.
Borrow indicates the carry flag used in subtraction operations.
Logical to share the carry flag for both addition and subtraction.
unioffaisalabad
www.tuf.edu.pk
Handling Carry in Addition

## Slide 33
Algorithm for 32-bit Subtraction
Subtract lower halves normally.
Use SBB for upper halves to handle potential borrows from lower halves.
Code Example:
      dest: dd 40000
      src: dd 80000
      mov ax, [src]
      sub word [dest], ax
      mov ax, [src+2]
      sbb word [dest+2], ax
unioffaisalabad
www.tuf.edu.pk
Extended Subtraction Algorithm

## Slide 34
We use extended shifting and extended addition to formulate our algorithm to do extended multiplication.
The multiplier is still stored in 16bits since we only need to check its bits one by one.
The multiplicand however cannot be stored in 16bits otherwise on left shifting its significant bits might get lost.
Therefore it has to be stored in 32bits and the shifting and addition used to accumulate the result must be 32bits as well.
unioffaisalabad
www.tuf.edu.pk
Extended Multiplication

## Slide 35
; 16bit multiplication
[org 0x0100]
jmp start
multiplicand: dd 1300 ; 16bit multiplicand 32bit space
multiplier: dw 500 ; 16bit multiplier
result: dd 0 ; 32bit result
start: mov cl, 16 ; initialize bit count to 16
mov dx, [multiplier] ; load multiplier in dx
checkbit: shr dx, 1 ; move right most bit in carry
jnc skip ; skip addition if bit is zero
mov ax, [multiplicand]
add [result], ax ; add less significant word
mov ax, [multiplicand+2]
adc [result+2], ax ; add more significant word
skip: shl word [multiplicand], 1
rcl word [multiplicand+2], 1 ; shift multiplicand left
dec cl ; decrement bit count
jnz checkbit ; repeat if bits left
mov ax, 0x4c00 ; terminate program
int 0x21
unioffaisalabad
www.tuf.edu.pk

## Slide 36
unioffaisalabad
www.tuf.edu.pk
Bitwise Logical Operations
What are Bitwise Logical Operations?
Operate at the bit level between two operands (byte or word).
Applied to corresponding bits in parallel across the entire operand.
Four main operations: AND, OR, XOR, and NOT.

## Slide 37
Performs a bitwise AND on corresponding bits.
A result bit is set only if both bits in the original operands are 1.
Example:
      and ax, bx
      and byte [mem], 5
unioffaisalabad
www.tuf.edu.pk
AND Operation
A | B | A AND B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table:

## Slide 38
Performs a bitwise OR on corresponding bits (inclusive OR).
A result bit is set if either or both bits in the original operands are 1.
Example:
      or ax, bx
      or byte [mem], 5
unioffaisalabad
www.tuf.edu.pk
OR Operation
A | B | A OR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Truth Table:

## Slide 39
Performs a bitwise XOR (exclusive OR) on corresponding bits.
A result bit is set if only one of the two bits is 1.
Important properties: XOR is reversible, widely used in cryptography and image processing.
Example:
      xor ax, bx
      xor byte [mem], 5
unioffaisalabad
www.tuf.edu.pk
XOR Operation
A | B | A XOR B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Truth Table:

## Slide 40
Inverts each bit of the operand (forms the one’s complement).
This is a single-operand instruction.
Unlike the other operations, NOT does not compare two operands.
Example:
        not ax
        not byte [mem]
unioffaisalabad
www.tuf.edu.pk
NOT Operation

## Slide 41
AND: Clearing bits, bit masking.
OR: Setting specific bits.
XOR: Reversible operations in cryptography, image manipulation.
NOT: Bit inversion, complement calculations
unioffaisalabad
www.tuf.edu.pk
Practical Applications of Bitwise Operations

## Slide 42
unioffaisalabad
www.tuf.edu.pk
Masking Operations
What are Masking Operations?
Masking is used to selectively manipulate certain bits in an operand.
Common masking operations: Selective Bit Clearing, Setting, Inversion, and Testing.
Operations involved: AND, OR, XOR, and TEST.

## Slide 43
Selective Bit Clearing with AND
AND is used to make selected bits zero while retaining others.
A mask with ones at positions to retain and zeroes where clearing is desired.
Example: To clear the lower nibble of a destination operand:
and ax, 0F0h
Result: Upper nibble remains unchanged, lower nibble is cleared.
unioffaisalabad
www.tuf.edu.pk
Selective Bit Clearing

## Slide 44
Selective Bit Setting with OR
OR sets selective bits based on the mask.
Bits are set where the mask has ones, other bits remain unchanged.
Example: To set the lower nibble of a destination operand:
or ax, 0Fh
Result: Upper nibble retains its value, lower nibble is set.
unioffaisalabad
www.tuf.edu.pk
Selective Bit Setting

## Slide 45
Selective Bit Inversion with XOR
XOR inverts bits based on the mask.
Only the bits corresponding to ones in the mask are inverted, while others remain unchanged.
Example: To invert the lower nibble of a destination operand
xor ax, 0Fh
Comparison with NOT: NOT inverts all bits, but XOR allows selective inversion.
unioffaisalabad
www.tuf.edu.pk
Selective Bit Inversion

## Slide 46
Selective Bit Testing with AND
AND can check if specific bits are set by applying a mask.
If the result is zero, the bit being tested was clear.
Example: To test if the lower nibble of a destination operand has any set bits:
                and ax, 0Fh
                jz clear_lower_nibble
Challenge: The AND operation modifies the destination operand.
unioffaisalabad
www.tuf.edu.pk
Selective Bit Testing

## Slide 47
Selective Bit Testing with TEST
TEST is similar to AND, but non-destructive.
Performs the AND operation and sets flags without altering the destination operand.
Example: To test if a specific bit is set without modifying the destination:
                test ax, 0Fh
                jz bit_clear
Usage: Useful in checking bits without affecting the operand.
unioffaisalabad
www.tuf.edu.pk
Non-Destructive Bit Testing with TEST

## Slide 48
Masking for Bit Testing in Multiplication
Previously used shifting and JC to test bits one by one in multiplication.
Masking simplifies testing specific bits at any position.
Allows for more efficient multiplication algorithms by avoiding the need to shift bits in sequence.
unioffaisalabad
www.tuf.edu.pk
Application in Multiplication Algorithms