## Slide 1: MIPS Architecture
A RISC-based Instruction Set Architecture

## Slide 2
MIPS (Microprocessor without Interlocked Pipeline Stages) architecture is a RISC (Reduced Instruction Set Computer) instruction set architecture (ISA) developed by MIPS Computer Systems.
It is widely used in embedded systems, digital devices, and educational contexts for learning computer architecture concepts.
unioffaisalabad
www.tuf.edu.pk
MIPS Architecture Overview

## Slide 3
RISC Design Philosophy:
  MIPS follows the RISC principles, which focus on:
    A small set of simple, uniform instructions.
    Fixed instruction size (32 bits in standard MIPS).
    Load/store architecture: Only load (LW) and store (SW) instructions access memory.
    Simple addressing modes.
Instruction Formats: MIPS uses three main instruction formats:
  R-type (Register-type): Used for arithmetic and logical instructions.
  Example: ADD $d, $s, $t → R[d] = R[s] + R[t]
  I-type (Immediate-type): Used for instructions with constants or addresses.
  Example: ADDI $t, $s, 10 → R[t] = R[s] + 10
  J-type (Jump-type): Used for jump instructions.
  Example: J 10000 → Jump to address 10000.
unioffaisalabad
www.tuf.edu.pk
Key Features of MIPS Architecture:

## Slide 4
unioffaisalabad
www.tuf.edu.pk
Key Features of MIPS Architecture:
Registers:
  MIPS has 32 general-purpose registers ($0 to $31) of size 32 bits.
  Register $0 always holds the value 0.
  Examples of registers:
    $s0-$s7: Saved registers for preserving values.
    $t0-$t9: Temporary registers for intermediate values.
    $a0-$a3: Argument registers for passing parameters.
    $v0, $v1: Return value registers.
Pipelining:
  MIPS uses pipeline processing to execute instructions efficiently.
  Instructions are divided into stages: IF (Instruction Fetch), ID (Instruction Decode), EX (Execute), MEM (Memory Access), and WB (Write Back).
Load/Store Architecture:
  MIPS separates memory access operations (LW, SW) from computation operations (ADD, SUB, etc.).
  Only load and store instructions access memory; all computations occur in registers.

## Slide 5
unioffaisalabad
www.tuf.edu.pk
Key Features of MIPS Architecture:
Endianness:
  MIPS supports both big-endian and little-endian byte ordering.
Instruction Set: The instruction set consists of:
  Arithmetic and logical instructions: ADD, SUB, AND, OR, XOR.
  Data transfer instructions: LW (Load Word), SW (Store Word).
  Control flow instructions: BEQ (Branch if Equal), BNE (Branch if Not Equal), J (Jump).
  Shift instructions: SLL (Shift Left Logical), SRL (Shift Right Logical).
MIPS Variants:
  MIPS32: 32-bit version of MIPS.
  MIPS64: 64-bit version of MIPS.
Applications:
  Embedded systems, gaming consoles (e.g., PlayStation 2), routers, and academic learning.

## Slide 6
The MIPS-I Memory Model and MMU (Memory Management Unit) are critical components of the MIPS architecture, defining how memory is accessed and managed in MIPS-based systems.
MIPS-I Memory Model
  Byte-Addressable Memory:
    The MIPS memory model is byte-addressable, which means that each memory address points to a single byte (8 bits).
    However, MIPS instructions typically work with words (4 bytes = 32 bits), so memory addresses must be aligned.
  Aligned Memory Access:
    Alignment requires that word addresses (32-bit values) start at memory addresses that are multiples of 4.
    Misaligned accesses (e.g., reading a word from address (0x1001) are not supported in MIPS-I and cause exceptions.
    Example:
    Address: 0x1000 0x1001 0x1002 0x1003 ← Word aligned
  Value: 0xDE 0xAD 0xBE 0xEF ← 4 bytes (word)
unioffaisalabad
www.tuf.edu.pk
MIPS-I Memory Model and MMU

## Slide 7
Memory Segmentation:
  MIPS divides its address space into specific regions, separating user mode and kernel mode operations.
    User Address Space: Typically ranges from 0x00000000 to 0x7FFFFFFF.
    Kernel Address Space: Higher addresses, reserved for OS and privileged access.
Endianness:
  MIPS supports both Big-endian and Little-endian byte orders.
    Big-endian: Most significant byte (MSB) stored at the lowest address.
    Little-endian: Least significant byte (LSB) stored at the lowest address.
  The system's endianness can be configured at startup.
unioffaisalabad
www.tuf.edu.pk
MIPS-I Memory Model and MMU
Address Range | Description
 | User space for applications.
0x80000000-0xFFFFFFFF | Kernel space (privileged mode).
0x00000000–0x7FFFFFFF

## Slide 8
MIPS-I MMU (Memory Management Unit)
  The Memory Management Unit (MMU) in MIPS is responsible for managing memory access, virtual memory, and address translation.
  Key Features of the MMU:
    Virtual Memory Support:
      The MMU allows processes to use virtual addresses instead of physical memory addresses.
      Virtual memory provides an illusion of a large, contiguous memory space, even if physical memory is fragmented.
    Page-Based Memory Management:
      The memory is divided into fixed-size pages (commonly 4 KB).
      The MMU maps virtual pages to physical frames in memory.
      Example:
      Virtual Address: 0x00401234 → Translates to Physical Address: 0x1F00234
unioffaisalabad
www.tuf.edu.pk

## Slide 9
unioffaisalabad
www.tuf.edu.pk
Translation Lookaside Buffer (TLB):
  The MMU uses a TLB to speed up address translation.
  The TLB is a small cache that stores recently accessed page table entries, avoiding repeated lookups in the page table.
  TLB Operations:
  TLB Hit: Address translation found in TLB → Fast access.
  TLB Miss: Address not in TLB → MMU performs a page table lookup.
Page Faults and Exceptions:
  If a program accesses an invalid virtual address (e.g., unmapped page), the MMU raises a page fault exception.
  The OS handles the page fault, either by:
    Loading the required page into physical memory.
    Terminating the process if access is invalid.
Kernel vs. User Mode:
  The MMU separates user mode and kernel mode memory.
  Kernel Mode: Provides privileged access to manage the system (e.g., I/O, device drivers).
  User Mode: Restricts access to user processes to prevent unauthorized operations.

## Slide 10
In MIPS, memory can only be accessed using load/store instructions:
  Load Instructions:
    Used to bring data from memory into registers.
    Example:
      LW $t0, 4($s0) # Load a word from address ($s0 + 4) into $t0
      LB $t1, 0($s1) # Load a byte from address ($s1 + 0) into $t1
  Store Instructions:
    Used to write data from registers back to memory.
    Example:
      SW $t2, 8($s0) # Store the word in $t2 to address ($s0 + 8)
      SB $t3, 0($s1) # Store the byte in $t3 to address ($s1 + 0)
Summary
The MIPS-I memory model uses a byte-addressable, word-aligned structure with support for both endianness modes.
Memory is divided into user space and kernel space, providing security and privilege separation.
The MMU in MIPS manages virtual memory, translating virtual addresses to physical addresses via page-based mapping and TLB.
Load and store instructions provide controlled access to memory, adhering to the load/store architecture principle of MIPS.
unioffaisalabad
www.tuf.edu.pk
MIPS Memory Access Instructions

## Slide 11
unioffaisalabad
www.tuf.edu.pk
The MIPS-I instruction set is a part of the MIPS architecture and follows the RISC (Reduced Instruction Set Computer) design philosophy.
It includes a simple and fixed set of instructions for efficient hardware implementation and software execution.
The MIPS-I instruction set consists of 32-bit fixed-length instructions divided into three main formats:
  R-type (Register): Used for arithmetic and logical operations.
    Example: ADD $d, $s, $t
  I-type (Immediate): Used for data transfer and branching.
    Example: LW $t, offset($s)
  J-type (Jump): Used for jump instructions.
    Example: J target
Each format corresponds to a specific class of operations, and they simplify instruction decoding and execution.
Types of Instructions:
  Arithmetic: ADD, SUB
  Logical: AND, OR, XOR
  Data Transfer: LW, SW
  Branching/Control: BEQ, BNE, J
  Shifting: SLL, SRL
MIPS-I Instruction Set

## Slide 12
unioffaisalabad
www.tuf.edu.pk
Opcode (6) | rs (5) | rt (5) | rd (5) | shamt (5) | funct (6)
R-Type (Register-Type) Instructions
  Used for arithmetic, logical, and shift operations that involve registers.
  Operates on data stored in registers.
  Instruction Format:
  Opcode: Specifies the operation type (always 0 for R-type instructions).
  rs: Source register 1.
  rt: Source register 2.
  rd: Destination register where the result is stored.
  shamt: Shift amount (used for shift instructions).
  funct: Function code to determine the exact operation (e.g., ADD, SUB).
Examples:
ADD: ADD $rd, $rs, $rt → Adds two registers.
ADD $t0, $t1, $t2 # $t0 = $t1 + $t2
SUB: SUB $rd, $rs, $rt → Subtracts two registers.
SUB $s0, $s1, $s2 # $s0 = $s1 - $s2
Instruction Formats in MIPS-I

## Slide 13
unioffaisalabad
www.tuf.edu.pk
Instruction Formats in MIPS-I
Logical Operations:
  AND: AND $rd, $rs, $rt
  OR: OR $rd, $rs, $rt
Shift Operations:
  SLL: SLL $rd, $rt, shamt (Shift Left Logical).
  SLL $t0, $t1, 2 # $t0 = $t1 << 2 (shift left by 2 bits)
Opcode (6) | rs (5) | rt (5) | Immediate (16)
I-Type (Immediate-Type) Instructions
  Used for immediate values, memory access, and branching.
  Includes a constant or address offset (immediate value).
  Instruction Format:
Opcode: Specifies the operation type.
rs: Source register.
rt: Destination register (or source/destination for memory instructions).
Immediate: 16-bit constant or address offset.

## Slide 14
unioffaisalabad
www.tuf.edu.pk
Instruction Formats in MIPS-I
Examples:
Immediate Arithmetic:
  ADDI: ADDI $rt, $rs, immediate → Adds immediate to a register.
ADDI $t0, $t1, 10 # $t0 = $t1 + 10
Memory Access Instructions (Load/Store):
  LW (Load Word): LW $rt, offset($rs) → Loads a word from memory.
LW $t0, 8($s0) # Load word at address $s0 + 8 into $t0
  SW (Store Word): SW $rt, offset($rs) → Stores a word into memory.
SW $t0, 8($s0) # Store word in $t0 to address $s0 + 8
Branch Instructions:
  BEQ (Branch if Equal): BEQ $rs, $rt, offset
BEQ $t0, $t1, LABEL # If $t0 == $t1, branch to LABEL
  BNE (Branch if Not Equal): BNE $rs, $rt, offset
BNE $t0, $t1, LABEL # If $t0 != $t1, branch to LABEL

## Slide 15
unioffaisalabad
www.tuf.edu.pk
Instruction Formats in MIPS-I
Opcode (6) | Target Address (26)
J-Type (Jump-Type) Instructions
  Used for unconditional jumps to specific addresses.
  Contains a large target address for branching.
  Instruction Format:
  Opcode: Specifies the operation type.
  Target Address: 26-bit immediate address (combined with PC during execution).
Examples:
  Jump Instruction:
    J: J target → Jumps to the specified address.
J 10000 # Jump to address 10000
  Jump and Link:
    JAL: JAL target → Jumps to address and saves return address in $ra.
JAL FUNCTION # Call FUNCTION and save return address

## Slide 16
unioffaisalabad
www.tuf.edu.pk
Types of Instructions in MIPS-I
MIPS-I includes the following types of instructions:
Arithmetic Instructions:
  ADD, ADDI, SUB, MUL, DIV
  Example:
ADD $t0, $t1, $t2 # $t0 = $t1 + $t2
Logical Instructions:
  AND, OR, XOR, NOR
  Example:
AND $s0, $s1, $s2 # $s0 = $s1 AND $s2
Shift Instructions:
  SLL (Shift Left Logical), SRL (Shift Right Logical), SRA (Shift Right Arithmetic)
  Example:
SLL $t0, $t1, 2 # $t0 = $t1 << 2

## Slide 17
unioffaisalabad
www.tuf.edu.pk
Types of Instructions in MIPS-I
Data Transfer Instructions:
  LW (Load Word), SW (Store Word), LB (Load Byte), SB (Store Byte)
  Example:
LW $t0, 4($s0) # Load word from memory SW $t1, 8($s0) # Store word to memory
Branch and Jump Instructions:
  BEQ (Branch if Equal), BNE (Branch if Not Equal)
  J (Jump), JAL (Jump and Link), JR (Jump Register)
  Example:
BEQ $t0, $t1, TARGET # Branch to TARGET if $t0 == $t1
Special Instructions:
  NOP (No Operation): Executes no action.

## Slide 18
unioffaisalabad
www.tuf.edu.pk
Types of Instructions in MIPS-I
Format | Opcode | rs | rt | rd / Immediate / Target
R | 6 bits | 5 bits | 5 bits | rd, shamt, funct (11 bits)
I | 6 bits | 5 bits | 5 bits | 16-bit immediate
J | 6 bits | 26-bit target address |  | 
Visual Representation of Formats

## Slide 19
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
The MIPS Register Convention defines how registers are used and what each register's role is within a program.
MIPS architecture follows a RISC (Reduced Instruction Set Computer) design, which means it relies heavily on a small set of fast registers for computation.
MIPS has 32 general-purpose registers, each 32 bits wide (in MIPS32), and they are denoted as $0 to $31.
To ensure consistency in programming and facilitate function calls, these registers are assigned specific conventions.

## Slide 20
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
Register Overview
MIPS registers are classified based on their usage convention into the following categories:
Register Name | Number | Usage
Zero Register | $zero | Always contains the value 0.
Assembler Reserved | $at | Reserved for assembler usage.
Function Arguments | $a0–$a3 | Pass arguments to functions.
Temporary Registers | $t0–$t9 | Temporary variables (caller-saved).
Saved Registers | $s0–$s7 | Preserved across function calls.
Return Value Registers | $v0–$v1 | Store return values from functions.
Global Pointer | $gp | Points to global/static data.
Stack Pointer | $sp | Points to the top of the stack.
Frame Pointer | $fp | Points to the base of the stack frame.
Return Address | $ra | Stores the return address for functions.

## Slide 21
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
MIPS has 32 general-purpose registers:
  $0: Always holds 0.
  $at: Reserved for assembler.
  $v0-$v1: Function return values.
  $a0-$a3: Arguments for function calls.
  $t0-$t9: Temporary registers (caller-saved).
  $s0-$s7: Saved registers (callee-saved).
  $gp: Global pointer.
  $sp: Stack pointer.
  $fp: Frame pointer.
  $ra: Return address.
Register Summary Table:
Register | Name | Usage
$0 | Zero | Constant value 0
$t0-$t9 | Temporaries | Temporary values
$s0-$s7 | Saved | Preserved across calls
$a0-$a3 | Arguments | Function arguments
$v0-$v1 | Return values | Function return values

## Slide 22
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
MIPS Register Breakdown
Special Purpose Registers
  $zero (Register 0):
    Always contains the value 0.
    Used when you need a constant zero value in operations.
    Example:
ADD $t0, $t1, $zero # $t0 = $t1 + 0
  $at (Assembler Temporary):
    Reserved for the assembler (pseudo-instructions).
    Not intended for general use by programmers.
Function Argument Registers
  $a0–$a3 (Registers 4–7):
    Used to pass up to 4 arguments to a function.
    If a function has more than 4 arguments, additional arguments are passed on the stack.
    Example:
ADDI $a0, $zero, 10 # Pass 10 as the first argument

## Slide 23
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
Temporary Registers
  $t0–$t9 (Registers 8–15, 24–25):
    Used for temporary variables within a function.
    Caller-saved: If a function needs these registers, it must save them before making a function call.
    Example:
ADD $t0, $t1, $t2 # Temporary result in $t0
Saved Registers
  $s0–$s7 (Registers 16–23):
    Used for variables that need to be preserved across function calls.
    Callee-saved: If a function modifies these registers, it must restore them before returning.
    Example:
ADD $s0, $s1, $s2 # $s0 is preserved

## Slide 24
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
Return Value Registers
  $v0–$v1 (Registers 2–3):
    Used to return values from functions.
    If a function returns a single value, it is stored in $v0.
    Example:
ADD $v0, $t0, $t1 # Function result in $v0
Stack Management Registers
  $sp (Stack Pointer):
    Points to the top of the stack.
    Used for function calls and local variables.
    Example:
SW $t0, 0($sp) # Store $t0 at top of the stack
  $fp (Frame Pointer):
    Points to the base of the current stack frame.
    Useful for accessing local variables within functions.

## Slide 25
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
Return Address Register
  $ra (Return Address):
    Stores the return address when a function is called.
    The return address is the instruction immediately after the JAL (Jump and Link) instruction.
    Example:
JAL FUNCTION # Jump to FUNCTION and save return address in $ra JR $ra # Return to saved address
Global Pointer
  $gp (Global Pointer):
    Points to the middle of the static data segment.
    Used to access global or static variables efficiently.

## Slide 26
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
Register Usage Rules
Caller-Saved Registers:
  $t0–$t9, $a0–$a3, $v0–$v1.
  The caller saves these registers before calling a function if needed.
Callee-Saved Registers:
  $s0–$s7.
  The callee (called function) saves and restores these registers.
Special-Purpose Registers:
  $sp must always point to the top of the stack.
  $ra must store the return address for proper function execution.

## Slide 27
unioffaisalabad
www.tuf.edu.pk
Register Convention in MIPS
Register | Number | Usage | Convention
$zero | 0 | Constant zero | Always 0
$at | 1 | Reserved for assembler | Assembler-specific
$v0–$v1 | 2–3 | Function return values | Caller saves
$a0–$a3 | 4–7 | Function arguments | Caller saves
$t0–$t9 | 8–15, 24–25 | Temporary variables | Caller saves
$s0–$s7 | 16–23 | Saved variables | Callee saves
$gp | 28 | Global pointer | Static data access
$sp | 29 | Stack pointer | Function stack
$fp | 30 | Frame pointer | Base of stack frame
$ra | 31 | Return address | Function return address
Register Convention Summary

## Slide 28
unioffaisalabad
www.tuf.edu.pk
Example Program:
.data
A: .word 5 # First number
B: .word 7 # Second number
C: .space 4 # Memory for result
.text
main:
lw $t0, A # Load A into $t0
lw $t1, B # Load B into $t1
add $t2, $t0, $t1 # $t2 = $t0 + $t1
sw $t2, C # Store result in C
li $v0, 10 # Exit syscall
syscall
Adding two numbers using MIPS assembly.