## Slide 1: Chapter 9
Real Time Interrupts and Hardware Interfacing

## Slide 2
Introduction to Hardware Interrupts
Definition:
  Real interrupts generated by external hardware.
INT Pin:
  Single external pin on the processor to receive hardware interrupts.
Purpose:
  Ensure real-time response to external events (e.g., key presses, printer status).
Why Hardware Interrupts?
Interrupts vs. Polling:
  Polling: Actively monitor devices, inefficient for the processor.
  Interrupts: Notify the processor only when needed, enabling multitasking.
Examples:
  Keyboard: Stores keypress during long computations.
  Printer: Signals when ready for new data.
unioffaisalabad
www.tuf.edu.pk

## Slide 3
Programmable Interrupt Controller (PIC)
Purpose:
  Manages multiple interrupt signals and forwards them to the processor.
Features:
  8 input lines (IRQ 0–7), 1 output signal to processor.
  Assigns priorities to IRQ lines (0 = highest priority).
Cascading PICs:
  IBM AT systems: Two PICs provide 16 interrupt sources (IRQ 0–15).
Priority Management in PIC
How it Works:
  Forward highest-priority interrupt to the processor.
  Lower-priority interrupts are queued until the higher-priority interrupt is serviced.
End Of Interrupt (EOI):
  Sent by the processor to signal completion of interrupt handling.
unioffaisalabad
www.tuf.edu.pk

## Slide 4
unioffaisalabad
www.tuf.edu.pk
IRQ | Function | Interrupt
IRQ 0 | Timer device | INT 8
IRQ 1 | Keyboard | INT 9
IRQ 2 | Cascade signal for 2nd PIC | INT A
IRQ 3 | Serial port (COM 2) | INT B
IRQ 4 | Serial port (COM 1) | INT C
IRQ 5 | Sound card/network card | INT D
IRQ 6 | Floppy disk drive | INT E
IRQ 7 | Parallel port | INT F
Interrupt Requests (IRQ) Lines and Their Functions

## Slide 5
IRQ to INT Mapping
Mapping by PIC:
  IRQ lines (0–7) → INT 8–F.
  Example:
    IRQ 0 → INT 8 (Timer interrupt).
    IRQ 1 → INT 9 (Keyboard interrupt).
Processor Perspective:
  Interrupt number is automatically generated by PIC without extra instructions.
unioffaisalabad
www.tuf.edu.pk

## Slide 6
Example: Timer Interrupt (IRQ 0 → INT 8)
Timer Chip:
  Generates interrupts at precise intervals.
  Handler updates system time.
Example Code Snippet:
; Timer Interrupt Handler Example
MOV AL, 20h ; EOI signal for PIC
OUT 20h, AL ; Send EOI to PIC
IRET ; Return from interrupt
unioffaisalabad
www.tuf.edu.pk

## Slide 7
unioffaisalabad
www.tuf.edu.pk
Handling Keyboard Interrupt (IRQ 1 → INT 9)
Keypress Handling:
  Stores keypress for later use.
Replacing the Interrupt Vector:
  Custom handler can be used to modify behavior.
Example Code Snippet:
; Keyboard Interrupt Handler Example
IN AL, 60h ; Read keypress from keyboard port
MOV [keybuffer], AL ; Store keypress
MOV AL, 20h ; EOI signal
OUT 20h, AL ; Send EOI to PIC
IRET ; Return from interrupt
keybuffer DB ? ; Buffer for storing keypress

## Slide 8
Key Takeaways
Hardware Interrupt Flow:
  IRQ → PIC → INT Pin → Processor → Interrupt Handler.
Important Concepts:
  IRQ to INT mapping.
  EOI signal for enabling lower-priority interrupts.
Best Practices:
  Properly handle and reset IRQs to avoid conflicts.
unioffaisalabad
www.tuf.edu.pk

## Slide 9
Introduction to I/O Ports
What are I/O Ports?
  Mechanism for processor to communicate with peripheral devices.
  Supports read and write operations.
Memory vs. I/O Ports
  Memory: Stores program data.
  Ports: Perform hardware control or interactions.
Peripheral Address Space
IBM PC Design: Separate memory and peripheral address spaces.
Memory Mapped I/O: Some processors map ports to memory cells.
Address Bus Usage: Lower 16 bits are used for I/O ports (65,536 possible ports).
unioffaisalabad
www.tuf.edu.pk

## Slide 10
unioffaisalabad
www.tuf.edu.pk
IN and OUT Instructions
Purpose: Read/write data from/to ports.
Key Points:
  MOV: Access memory space.
  IN and OUT: Access peripheral address space.
Example Instructions:
in al, 0x21 ; Read from port 21
out 0x21, al ; Write to port 21
mov dx, 0x378
in al, dx ; Read from port in DX
out dx, al ; Write to port in DX

## Slide 11
PIC Ports
Ports 20 and 21:
  Port 20: Control Port.
  Port 21: Interrupt Mask Register (IMR).
Interrupt Masking:
  Bit 0-7: Correspond to IRQ lines.
  0: Enable interrupt.
  1: Disable interrupt.
unioffaisalabad
www.tuf.edu.pk
Example Program: Disable Keyboard Interrupt
Purpose: Disable IRQ 1 for the keyboard.
Code:
in al, 0x21 ; Read IMR
or al, 2 ; Set bit for IRQ 1
out 0x21, al ; Write back to IMR
mov ax, 0x4c00 ; Terminate program
int 0x21
Result: Keyboard interrupts are stopped.

## Slide 12
Keyboard Scan Codes
Key Features:
  Each key press/release sends a scan code.
  Press Code: Most Significant Bit (MSB) = 0.
  Release Code: MSB = 1.
Examples:
  Shift-A Sequence:
    Shift Press Code
    A Press Code
    A Release Code
    Shift Release Code
unioffaisalabad
www.tuf.edu.pk
Interrupt Chaining
Definition: Allows original ISR to function after custom ISR completes.
Steps:
  Save the address of the original ISR.
  Jump to it at the end of the custom ISR using JMP FAR.

## Slide 13
Terminate and Stay Resident (TSR) Programs
Purpose: Retain part of a program in memory after termination.
Difference in Termination Methods:
  INT 21h, Service 4C: Releases all memory.
  INT 21h, Service 31: Retains a portion of memory.
Memory Allocation for TSR
DOS Memory Structure:
  Reserved Areas: Interrupt Vector Table, BIOS/DOS data, COMMAND.COM.
  Transient Program Area: For loaded programs.
Freemem Pointer: Adjusted to allocate or reclaim memory.
unioffaisalabad
www.tuf.edu.pk

## Slide 14
unioffaisalabad
www.tuf.edu.pk
Calculating Resident Memory
Steps:
  Place a label at the end of the required code.
  Calculate bytes to retain.
  Round up using: (bytes + 15) / 16.
Example:
  100 bytes → 7 paragraphs (rounded).
TSR Program Example
Goal: Display L for left shift and R for right shift.
Features:
  Captures scan codes.
  Prevents shift keys from being forwarded to BIOS.
Command: Verify resident program using mem /c.

## Slide 15
unioffaisalabad
www.tuf.edu.pk
Conclusion
I/O Ports: Enable hardware communication and control.
IN/OUT Instructions: Facilitate port data manipulation.
TSR Programs: Extend operating system functionality by retaining memory.

## Slide 16
unioffaisalabad
www.tuf.edu.pk
Introduction to Programmable Interval Timer (PIT)
What is PIT?
  A peripheral device used to generate precise time intervals.
  Chip model: 8254.
Fixed Frequency:
  Input frequency: 1.19318 MHz.
  Independent of processor clock speed.
Divisor and Timer Tick
16-bit Divisor: Divides the input frequency to control the output.
Special Case: Divisor of 0 → 65536.
Default Behavior:
  Divisor: 65536.
  Timer Tick Frequency: 18.2 Hz (1193180/65536).
  Interval Between Ticks: 55ms.

## Slide 17
unioffaisalabad
www.tuf.edu.pk
PIT and System Time
Purpose:
  Maintains system time with precise intervals.
  Triggers IRQ 0 to handle system clock.
High Priority Interrupt:
  Breaks execution of other processes.
  Used for time-sensitive operations.
PIT in TSR Programs
Integration with TSR:
  TSR programs rely on interrupt hooking for activation.
  PIT's precise interrupts are ideal for periodic tasks.
Timer Interrupt:
  Hooked to perform custom actions (e.g., updating a tick count).

## Slide 18
unioffaisalabad
www.tuf.edu.pk
Objective: Hook the timer interrupt to display tick count.
Code:
[org 0x0100] ; Origin for emu8086
jmp start ; Jump to start of the program
old_isr dw 0 ; Placeholder for original interrupt vector
start:
; Save old timer interrupt vector
push es
mov ax, 0
mov es, ax
mov bx, 0x1C * 4 ; Interrupt 1Ch vector
mov ax, es:[bx]
mov [old_isr], ax
mov ax, es:[bx + 2]
mov [old_isr + 2], ax
; Hook new interrupt
cli
lea ax, new_isr
mov es:[bx], ax
mov ax, cs
mov es:[bx + 2], ax
sti
Example: Hooking Timer Interrupt
; Terminate and Stay Resident
mov dx, end - start + 15
shr dx, 4 ; Convert bytes to paragraphs
mov ah, 0x31
int 0x21
new_isr:
; Custom handler
push ax
push cx
push dx
; Increment tick count
mov dx, tick_count
inc word [dx]
; Restore old handler
call far [old_isr]
pop dx
pop cx
pop ax
iret
tick_count dw 0 ; Counter to hold tick count
end:
Features:
  Hooks INT 1Ch (timer interrupt).
  Updates and displays a tick counter.

## Slide 19
unioffaisalabad
www.tuf.edu.pk
Key Points to Remember
PIT Features:
  Fixed input frequency ensures precision.
  Generates periodic IRQ 0 interrupts.
TSR Integration:
  Control is interrupt-driven, never directly returned.
  PIT enables periodic tasks for TSRs.
Conclusion
PIT: A versatile peripheral device for system timing.
Assembly Programming: Provides direct access to PIT functionality.
TSR Usage: Combines with PIT for interrupt-driven applications.

## Slide 20
unioffaisalabad
www.tuf.edu.pk
Introduction to Parallel Ports
Purpose:
  Enable computers to control external hardware.
  Examples: Controlling LEDs, sending signals to printers, or other devices.
Types of Ports:
  Parallel Port, Serial Port, USB, FireWire.
Focus: Parallel Port (DB-25).
Parallel Port Connector
Connector:
  DB-25: A 25-pin connector.
  Bidirectional communication.
Pin Overview:
  Pins 2-9: Data pins (Processor → Device).
  Pin 10 (ACK): Acknowledges receipt of data.
  Pins 18-25: Ground (Electrical reference point).

## Slide 21
unioffaisalabad
www.tuf.edu.pk
Parallel Port Control
Processor View:
  Processor communicates via parallel port controller, not directly with pins.
Ports for LPT1:
  378: Data port (sends data to pins 2-9).
  37A: Control port (manages IRQ and ACK signals).
Voltage Levels:
  1 bit: 5V on corresponding pin.
  0 bit: 0V on corresponding pin.
Control Port (37A)
Bit 4: Enables IRQ 7 triggering via ACK (Pin 10).
Common Applications:
  Sending scancodes of pressed keys to external hardware (e.g., LEDs).

## Slide 22
unioffaisalabad
www.tuf.edu.pk
Circuit Example: LED Control
Circuit Setup:
  8 LEDs connected to data pins (Pins 2-9).
  Ground pins (18-25) connected to circuit ground.
Functionality:
  LEDs light up based on the data sent to port 378.
  Binary data from the processor is converted to voltage signals.
  Example Program: Sending Scancodes to LEDs
  [org 0x0100] ; Origin for emu8086
  jmp start ; Jump to start of program
  start:
  ; Keyboard hook setup
  mov ah, 0x09 ; INT 09H keyboard interrupt
  mov dx, old_int
  int 0x21 ; Save old interrupt vector
  mov ah, 0x25 ; Set new interrupt vector
  lea dx, new_isr
  int 0x21
  ; Stay resident
  mov dx, end - start + 15
  shr dx, 4 ; Convert bytes to paragraphs
  mov ah, 0x31
  int 0x21
  new_isr:
  ; Read scan code
  in al, 0x60 ; Read keyboard scan code
  out 0x378, al ; Send to parallel port
  iret ; Return from interrupt
  old_int dw 0 ; Placeholder for original ISR address
  end:

## Slide 23
unioffaisalabad
www.tuf.edu.pk
Key Points to Remember
Parallel Port Pins:
  Pins 2-9: Data transmission.
  Pin 10 (ACK): Interrupt signaling (IRQ 7).
Voltage Representation:
  1 = 5V, 0 = 0V.
Practical Example: Sending keyboard scancodes to LEDs.
Conclusion
Parallel Ports: Essential for interfacing computers with external hardware.
Assembly Programming: Provides direct control of data and signals.
Applications: Light control, printers, custom hardware projects.