## Slide 1: Chapter 8
Software Interrupts

## Slide 2
Introduction to Interrupts
Definition: Interrupts are asynchronous events external to the processor.
Key Characteristics:
  Asynchronous: Occur independently of the processor's current operation.
  Unpredictable: Exact timing of occurrence cannot be anticipated.
Importance: Allow the processor to respond to external events.
unioffaisalabad
www.tuf.edu.pk

## Slide 3
Types of Interrupts in 8088 Processor
1. Hardware Interrupts:
  Generated by external hardware.
  Examples: Pressure sensors, external signals.
2. Software Interrupts:
  Generated within the processor.
  Act as an extended far call mechanism.
  Pushes FLAGS, CS, and IP onto the stack.
unioffaisalabad
www.tuf.edu.pk

## Slide 4
unioffaisalabad
www.tuf.edu.pk
Software Interrupt Mechanism
INT Instruction:
  Syntax: INT n (where n is 0-255).
  Executes Interrupt Service Routine (ISR).
Interrupt Vector Table (IVT):
  Location: Physical memory address 0.
  Size: 1 KB (256 vectors × 4 bytes each).
  Format:
    First 2 bytes: Offset of ISR.
    Next 2 bytes: Segment of ISR.

## Slide 5
Operation of INT Instruction
Microcode steps:
  Push FLAGS, CS, and IP onto the stack.
  Disable interrupts by clearing IF and TF flags.
  Load CS and IP with ISR address from IVT.
Operation of IRET Instruction
Microcode steps:
  Pop IP, CS, and FLAGS from the stack.
  Restore original state of IF and TF.
  Return to the interrupted program.
unioffaisalabad
www.tuf.edu.pk

## Slide 6
Interrupts Reserved by 8088
INT 0: Division by zero.
  Triggered by a DIV instruction if the quotient doesn't fit.
INT 1: Trap (Single Step Interrupt).
  Used in debugging.
INT 2: Non-Maskable Interrupt (NMI).
  Used for critical failures (e.g., hardware failure).
INT 3: Debug Interrupt.
  Single-byte opcode, used in debuggers.
INT 4: Arithmetic Overflow.
  Triggered by INTO instruction when the overflow flag is set.
unioffaisalabad
www.tuf.edu.pk

## Slide 7
unioffaisalabad
www.tuf.edu.pk
Aspect | Hardware Interrupts | Software Interrupts
Generated by | External hardware | Processor itself
Trigger mechanism | Signal on INT or NMI pin | INT instruction
Interrupt handler | Address in IVT | Address in IVT
Hardware vs. Software Interrupts
Real-Time Interrupts (Overview)
Used for:
  Control Applications: e.g., closing a valve in response to a sensor.
  Critical System Responses: Handling urgent hardware events.

## Slide 8
Flexibility of IVT
Mapping Mechanism:
  Address of ISR can be changed dynamically.
  Enables flexible control of interrupt handling.
Summary
Key Concepts:
  INT and IRET operation.
  IVT and its structure.
  Reserved interrupts in 8088.
Applications:
  Debugging, control systems, and hardware failure management.
unioffaisalabad
www.tuf.edu.pk

## Slide 9
BIOS and DOS Interrupts
Purpose of Interrupts in IBM PCs:
  Enable user programs to access system services for hardware (e.g., floppy drive, VGA, clock).
  Avoids the need to understand detailed hardware mechanisms.
BIOS and Firmware:
  BIOS (Basic Input Output Services): Interface to basic hardware.
  Firmware: Software burned into ROM by the manufacturer.
  BIOS Services: Low-level services for hardware control.
BIOS Role in Boot Process
Boot Sequence:
  BIOS gains control after power-on at a fixed address.
  Executes hardware testing and initializes bootstrap to load OS.
Layers of Abstraction:
  Hardware → BIOS Services → OS Services.
  BIOS provides device-independent services like clearing the screen, displaying characters, etc.
unioffaisalabad
www.tuf.edu.pk

## Slide 10
Interrupt Mechanism for BIOS
Why Use Interrupts?
  Flexible mechanism for accessing firmware services.
  Allows manufacturers to place routines at any memory location.
BIOS Interrupts:
  Examples:
    INT 10: Video services.
    INT 16: Keyboard services.
    INT 17: Parallel port services.
DOS Interrupts
Single Entry Point:
  INT 21: Access to all DOS services.
  Services identified by Service Numbers in registers.
Service Numbers:
  Service number often in AH.
  Sub-services in AL or BL.
unioffaisalabad
www.tuf.edu.pk

## Slide 11
BIOS Interrupt Service Numbers
Service Numbering Scheme:
  Example: INT 10 Service 0 → Character printing.
  Allows efficient multiplexing of services within an interrupt.
Arguments in Interrupts:
  Passed via registers (not the stack).
  Documented per service and sub-service.
Example: INT 10 Service 13
Program Objective: Print a string using BIOS video services.
Why BIOS Works Universally:
  Independent of video memory location or hardware specifics.
unioffaisalabad
www.tuf.edu.pk

## Slide 12
; print string using bios service
[org 0x0100]
jmp start
message: db 'Hello World'
start: mov ah, 0x13 ; service 13 - print string
mov al, 1 ; subservice 01 – update cursor
mov bh, 0 ; output on page 0
mov bl, 7 ; normal attrib
mov dx, 0x0A03 ; row 10 column 3
mov cx, 11 ; length of string
push cs
pop es ; segment of string
mov bp, message ; offset of string
int 0x10 ; call BIOS video service
mov ax, 0x4c00 ; terminate program
int 0x21
unioffaisalabad
www.tuf.edu.pk