## Slide 1: Chapter 6
Display Memory

## Slide 2
unioffaisalabad
www.tuf.edu.pk
Debugger's Role in Assembly Programming
Debugger: A Key Tool
  Provides a close view of the processor.
  Enables execution and monitoring of each instruction.
Why Use Debugger?
  Many bugs become visible only with instruction-level monitoring.
  Essential for assembly language program development.
Displaying Characters in DOS Character Mode
Character Mode in DOS
  Specific to IBM PC.
  Uses the Video Graphics Adapter (VGA).
How Characters Are Displayed
  Characters are stored and processed as numbers.
  VGA interprets these numbers to display shapes.
  Pixels glow for "1" and turn off for "0".

## Slide 3
What is ASCII?
  American Standard Code for Information Interchange.
  Standard numeric representation of characters.
Universal Compatibility
  ‘A’ on one system is ‘A’ on another.
  Enables global communication and consistency.
ASCII Table and Standards
Standard ASCII
  128 characters, numbered 0–127.
Extended ASCII
  Introduced by IBM PC.
  Adds 128 more characters (total: 256, 0–255).
  Includes line drawings, corners, and non-English characters.
Key Features
  Standard ASCII: Official standard.
  Extended ASCII: Industry standard for IBM PC peripherals.
unioffaisalabad
www.tuf.edu.pk
ASCII Codes

## Slide 4
unioffaisalabad
www.tuf.edu.pk
ASCII in Practice
Applications of ASCII
  Printers: Understand ASCII to print characters.
  Displays: VGA cards render shapes based on ASCII codes.
  Communication: ASCII ensures data consistency across systems.
Important ASCII Ranges
Character Groups in ASCII
  Uppercase Letters: 41-5A (Hexadecimal)
  Lowercase Letters: 61-7A (Hexadecimal)
  Numbers: 30-39 (Hexadecimal)
Contiguous Arrangement Benefits
  Convert case: Add/Subtract 0x20.
  Convert digit to ASCII: Add 0x30.

## Slide 5
unioffaisalabad
www.tuf.edu.pk
Display Memory Formation
Display Memory and ASCII Codes
VGA Interpretation
  Sending 0x40 displays the visual representation of 'A'.
  Display is an interpretation of ASCII codes.
Memory Mapping
  Video memory seen as a block of system memory.
  ASCII placed in video memory corresponds to a character on screen.
Mapping Memory to Screen
Screen Dimensions
  80 rows × 25 columns.
Memory Mapping
  Video memory is linear, mapped to 2D screen space.
  Each character uses 1 word:
    Lower Byte: ASCII code.
    Higher Byte: Attribute (color, intensity, blinking).

## Slide 6
unioffaisalabad
www.tuf.edu.pk
Display Memory Formation
Video Memory Address
Standard Base Address
  VGA text mode color display starts at physical address B8000.
Uniformity Across Systems
  Enables software to work across different video cards.
  First byte at B8000: ASCII of top-left character.
Attribute Byte in Video Memory
Attribute Byte Structure
  Bit 7: Blinking of foreground character.
  Bits 6–4: Background color (RGB).
  Bits 3–0: Foreground color (RGB + Intensity).
Color Combinations
  Foreground: 16 colors.
  Background: 8 colors.

## Slide 7
unioffaisalabad
www.tuf.edu.pk
Display Memory Formation
Practical Examples of Display Memory
Writing to Memory
  mov ax, 0xb800
  mov es, ax (Set ES to video memory).
Examples:
  Top-Left Corner:
    mov word [es:0], 0x0741 (White 'A' on black).
  Second Line, First Column:
    mov word [es:160], 0x1230 (Green '0' on blue).

## Slide 8
[org 0x0100]
mov ax, 0xb800 ; Load video base
mov es, ax ; Point ES to video base
mov di, 0 ; Point DI to top-left
nextchar:
mov word [es:di], 0x0720 ; Clear char
add di, 2 ; Move to next location
cmp di, 4000 ; Check end of screen
jne nextchar ; Repeat if not done
mov ax, 0x4c00 ; Terminate program
int 0x21
unioffaisalabad
www.tuf.edu.pk
Clearing the Screen Example

## Slide 9
unioffaisalabad
www.tuf.edu.pk
Key Observations
Details in Screen Clearing
  Code for space: 0x20.
  Attribute for white on black: 0x07.
  Each location is 2 bytes (character + attribute).
Screen Size Calculation
  80 rows × 25 cols × 2 bytes = 4000 bytes.
Output Verification
Execution
  Cannot observe in debugger as it overwrites screen.
  Direct execution (COM file) clears the screen.
Output
  Screen clears, and command prompt reappears after program termination.

## Slide 10
unioffaisalabad
www.tuf.edu.pk
  Number Printing in Assembly Language
The Challenge of Number Printing
Problem:
  Numbers are stored as binary values, not ASCII.
  Example: 10 is stored as binary 1010 (not ASCII '1' and '0').
Issue:
  Direct display of raw binary numbers is meaningless on screen.
  Solution: Convert numbers to ASCII representation.
Key Steps in Number Conversion
  Divide the number by the base (10 for decimal).
  Extract the remainder (rightmost digit).
  Convert the remainder to ASCII (add 0x30 for decimal).
  Save the ASCII digit on the stack.
  Repeat for the quotient until it becomes zero.
  Pop digits from the stack and display in correct order.

## Slide 11
Algorithm for Number Printing
Input: Number in binary format.
Process:
  Divide number by base.
  Push ASCII representation of remainder onto stack.
  Repeat until quotient is zero.
  Pop digits from stack to display left-to-right.
Output: Correct ASCII representation of the number.
Using the Stack to Reverse Order
Problem:
  Digits are processed right-to-left.
Solution:
  Use the Last In First Out (LIFO) nature of the stack.
  Push digits: Rightmost first.
  Pop digits: Leftmost first.
unioffaisalabad
www.tuf.edu.pk
  Number Printing in Assembly Language

## Slide 12
unioffaisalabad
www.tuf.edu.pk
  Number Printing in Assembly Language
Overview of the DIV Instruction
Purpose: Integer division.
Modes of Operation:
  16-bit dividend (AX):
    DIV BL divides AX by an 8-bit operand (BL).
    Quotient in AL, Remainder in AH.
  32-bit dividend (DX:AX):
    DIV BX divides DX:AX by a 16-bit operand (BX).
    Quotient in AX, Remainder in DX.
Division Errors
Divide Overflow Error:
  Occurs when quotient exceeds destination capacity.
  Example: Division by zero.
Handling:
  A type 0 interrupt is generated.
  Result is undefined, and program terminates.

## Slide 13
unioffaisalabad
www.tuf.edu.pk
  Number Printing Example Code
mov ax, number ; Load the number to print
mov bx, 10 ; Set base (decimal)
mov cx, 0 ; Clear counter for digits
print_loop:
xor dx, dx ; Clear DX (high word of dividend)
div bx ; AX = AX / BX, Remainder in DX
add dl, 0x30 ; Convert remainder to ASCII
push dx ; Push ASCII digit onto stack
inc cx ; Increment digit count
test ax, ax ; Check if quotient is zero
jnz print_loop ; Repeat if not zero
print_digits:
pop dx ; Pop ASCII digit
; Add your screen printing logic here
loop print_digits ; Repeat for all digits

## Slide 14
unioffaisalabad
www.tuf.edu.pk
  Number Printing Example Code
Key Points to Remember
Conversion Process:
  Dividing by base extracts digits.
  Adding 0x30 converts to ASCII.
Role of Stack:
  Corrects the display order of digits.
DIV Instruction:
  Handles unsigned integer division.
Practical Significance
Applications:
  Printing numbers in any base (decimal, hexadecimal, etc.).
  Foundation for advanced display operations.
Learning Outcome:
  Understanding low-level number handling and display in assembly.

## Slide 15
unioffaisalabad
www.tuf.edu.pk
  Screen Location Calculation
Introduction to Screen Location
Problem:
  Display at specific positions on the screen with customizable attributes.
Solution:
  Map 2D screen coordinates (row, column) to 1D video memory.
Concept:
  Memory location = (row * 80 + column) * 2
  Two bytes per character in video memory:
    Byte 1: ASCII code.
    Byte 2: Attribute (color, blinking, etc.).
Multiplication in Coordinate Mapping
Steps:
  Multiply row number by 80 (columns per row).
  Add column number to get the linear memory location.
  Multiply by 2 (each character occupies two bytes).
Formula: location = (row * 80 + column) * 2

## Slide 16
unioffaisalabad
www.tuf.edu.pk
  Screen Location Calculation
MUL Instruction Overview
Purpose: Perform unsigned multiplication.
Operation Modes:
  8-bit operand:
    Multiply source with AL.
    Result in AH:AL (16-bit).
  16-bit operand:
    Multiply source with AX.
    Result in DX:AX (32-bit).
MUL Instruction Details
Syntax: MUL source
Examples:
  MUL BL (8-bit):
    AL * BL → Result in AH:AL.
  MUL BX (16-bit):
    AX * BX → Result in DX:AX.
Result Storage:
  Low part: AL or AX.
  High part: AH or DX.

## Slide 17
unioffaisalabad
www.tuf.edu.pk
  Screen Location Calculation
Calculating Screen Location
Input:
  row, column, attribute.
Process:
  Multiply row * 80.
  Add column.
  Multiply result by 2.
  Use this memory location to store ASCII and attribute bytes.
String Printing at Desired Location
Parameters:
  x-position (column).
  y-position (row).
  attribute.
Steps:
  Calculate memory location: location = (row * 80 + column) * 2.
  Write string to calculated memory location.
  Include attribute for each character.

## Slide 18
unioffaisalabad
www.tuf.edu.pk
  Example Program
mov ah, row ; Load row
mov al, 80 ; 80 columns per row
mul al ; row * 80 → result in AX
add ax, column ; Add column
shl ax, 1 ; Multiply by 2 (shift left by 1)
mov bx, ax ; Store location in BX
mov di, bx ; DI points to video memory location
; Now write ASCII and attribute to video memory
mov [es:di], ascii ; Write ASCII character
mov [es:di+1], attr ; Write attribute

## Slide 19
unioffaisalabad
www.tuf.edu.pk
Applications
Custom Display:
  Print at specific locations on the screen.
  Use attributes for foreground/background colors and effects.
Dynamic Output:
  Create menus, formatted text, and interactive programs.
Summary
Screen Mapping Formula: (row * 80 + column) * 2.
MUL Instruction: Efficient multiplication in assembly.
Custom Positioning: Enables dynamic and interactive display output.