## Slide 1: Computer Organization & Assembly Language
3 – System Bus & Register

## Slide 2: Outline
  The Components of Microcomputer System
    System Bus
      Data, Address & Control
    The CPU
      Registers

## Slide 3: System Bus

## Slide 4: What is a Bus?
A communication pathway connecting two or more devices
Often grouped
  A number of channels in one bus
  e.g. 32-bit data bus is 32 separate single bit channels
CPU
Memory
I/O
Address Bus
Control Bus
Data Bus

## Slide 5: Data Bus
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width is a key determinant of performance
  8, 16, 32, 64 bit

## Slide 6: Address bus
Identify the source or destination of data
  e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64k address space

## Slide 7: Control Bus
Control and timing information
  Memory read/write signal
  Interrupt request
  Clock signals

## Slide 8: Types of Transfer
Memory to Processor
Processor to Memory
I/O to Processor
Processor to I/O
I/O to and from Memory

## Slide 9: Interconnection Structure
Memory
  N words of equal length, each word having a unique address
  Unit of Transfer (read/Write): Word
  Operation: Read/Write indicated by Control Signal
  Location of operation specified by an address
I/O Module (Middleman)
  Two operations: read and write
  May control other external devices
  Port: interface between I/O module and device
  Able to send interrupt signal to CPU

## Slide 10: Contd..
  CPU
  Reads in instruction and data
  Writes out data
  Uses control signal to control all operations
  Receives interrupt signal

## Slide 11
Address
Data Read
Data Write
Interrupt Signals

## Slide 12: Registers

## Slide 13: Registers
Registers are high-speed storage locations inside the microprocessor.
Designed to be accessed at much higher speed than conventional memory.
Registers are classified according to the functions they perform.
General Types of Registers:
  Data Registers: To hold data for an operation.
  Address Registers: To hold the address of an instruction or data.
  Status/Flag Register: keeps the current status of the processor or result of an arithmetic operation.

## Slide 14: 8086 Internal registers 16 bits (2 bytes each)
AX, BX, CX and DX are two
bytes wide and each byte can
be accessed separately
These registers are used as
memory pointers.
Segment registers are used
as base address for a segment
6 status; 3 control ; 7 unused

## Slide 15: General Purpose/Data Registers
Following four registers are available to the programmer for general data manipulation:
AX (Accumulator): Used in arithmetic, logic and data transfer instructions. Also required in multiplication, division and input/output operations.
BX (Base): It can hold a memory address that points to a variable.
CX (Counter): Act as a counter for repeating or looping instructions. These instructions automatically repeat and decrement CX and quit when equals to 0.
DX (Data): It has a special role in multiply and divide operations. Also used in input/output operations.

## Slide 16: Segment Registers
Store addresses of instruction and data in memory.
These values are used by the processor to access memory locations.
CS (Code): Defines the starting address of the section of memory holding code.
DS (Data): Defines the section of memory that holds most of the data used by programs.
ES (Extra): This is an additional data segment that is used by some of the string instructions.
SS (Stack): It defines the area of the memory used for stack

## Slide 17: Pointers and Index Registers
These can be accessed only as 16 bit registers.
IP - instruction pointer: Always points to next instruction to be executed. IP register always works together with CS segment register and it points to currently executing instruction.
SI - source index register: Can be used for pointer addressing of data. Offset address relative to DS
DI - destination index register: Can be used for pointer addressing of data . Offset address relative to ES
SI and DI used in string movement instructions.
SP and BP are used to access data inside the stack segment
BP - base pointer: Primarily used to access parameters passed via the stack. Offset address relative to SS
SP – stack pointer: Always points to top item on the stack. Offset address relative to SS

## Slide 18: 80386 Extended Registers
The 80386/80486 processor contain 32-bit registers which greatly improve the efficiency of program that take advantage of them.
  EAX, EBX, ECX, EDX,
  EFLAGS
  EIP
  EBP, ESP, ESI, EDI.